## Slide 1: Machine Learning Application in Optimization of woven two-layered hydraulic pipes
Presented By-
Dushyant Singh Udawat, Undergrad, IIT - Roorkee
Indian Institute Of Technology Roorkee
Notes: Add UBC logo + your University logo

## Slide 2: Table of Contents
Product Description
  Two-layered Woven Hydraulic Pipe.
  Snaking Issue
  Overall Objective
Data Summary
Stages I – Pre-analysis of data
  Excel
  Insights discussion
Stage II – MACHINE LEARNING PREDICTION MODELS
  Procedure to select best models
  Model performances for dataset
  Model Comparison
Stage III – Explainable AI
  LIME and SHAP comparison and selection of SHAP
  SHAP Insights
Next Steps
  Optimization

## Slide 3: Product Description
Two-layered Woven Composite Hydraulic Pipe
  Expected Application
    to transport working fluids (e.g., water for oil and gas firefighting, water sand slurries in mining activities, among others
Snaking Issue
  axial buckling of the hose structure under pressurized, causing interference with other personnel or equipment on the worksite
  Implications on finance
  Challenges
  That’s why the use of Machine Learning
Notes: Explainations –
There is a two layered pipe here which

## Slide 4: Overall Objectives
Reduce the Number of Snaking, Snaking Length, Snaking Amplitude in the hose in such a way as to decrease the cost to the company.
Get Insights on the data provided.
Make prediction models to predict the snaking in a hose.
Provide the manufacturer with an AI-based decision-making tool.

## Slide 5: Data Summary - Inputs
We have four Parameters:
  Inner Modulus
  Outer Modulus
  Axial Load
  Friction factor between the
  hose and ground.
These Parameters are changeable either during operations or during design process. Simulations gives us the data which is then used in Machine Learning methods to give predictions and get insights.
The data is generated for five values of each parameter. Therefore, giving a total of 5*5*5*10 1250 samples.
Parameter Name | Units | Input Variables Min-Max (Levels)
Inner Modulus |  | 0.10-0.18 (5)
Outer Modulus |  | 0.07-0.15 (5)
Axial Load |  | 6-14(5)
Friction Coefficient | - | 0.01 – 45 (10)
Parameter Name | Units | Input Variables Min-Max (Levels)
Inner Modulus |  | 0.10-0.18 (5)
Outer Modulus |  | 0.07-0.15 (5)
Axial Load |  | 6-14(5)
Friction Coefficient | - | 0.01 – 45 (10)
Notes: (are simulations 100percent correct ?)

## Slide 6: Data Summary - Outputs
Output Data Description
  We have three output variables regarding snaking behavior
    Snaking Length,
    No. of Snaking,
    Snaking Amplitude.
  Their Description is as shown in the table.
  Their Correlation with input variables can be seen in the adjoining figure.
Parameter Name | Units | Input Variables Min-Max (Levels)
Number of Snaking | - | 0-14 (7.72)
Snaking Length |  | 0-49 (31)
Snaking Amplitude |  | 0-6.64 (2.31)
Parameter Name | Units | Input Variables Min-Max (Levels)
Number of Snaking | - | 0-14 (7.72)
Snaking Length |  | 0-49 (31)
Snaking Amplitude |  | 0-6.64 (2.31)
Notes: (are simulations 100percent correct ?)

## Slide 7: STAGE I Pre-Analysis of Data

## Slide 8
Axial load
Inner Modulus
Outer Modulus
Snaking Amplitude
Number of Snaking
Snaking Length

## Slide 9: Insights
The single most important factor is the axial Load, the values changes a lot as we increase the loads from 6kN to 8kN.
After load>6kN, the variation in output parameters from modulus is less. This is corroborated by Linear Regression on separate Data, when Axial Load = 6 kN, and axial load > 6kN.

## Slide 10
After load>6kN, the variation in output parameters from modulus is lesser. ( Linear Regression on separate Data)
After Axial Load > 6kN, Role of Inner Modulus is more important than Outer Modulus.
Generally, as inner and outer modulus increases, the tendency for snaking reduces slightly (Correlation)
For zero Snaking Condition –
Axial load < 7kN, Inner modulus > 0.13, Outer modulus> 0.13.
No dependence on the friction coefficient
(Correlation, Explainable AI, Models testing)

## Slide 11: ANOVA
ANOVA Analysis Shows – (Show fig. for Number of Snaking)
Significant Variables – Inner , Outer and Axial load.
Insignificant = Friction and all its interactions.
Interaction between inner and outer modulus is Insignificant. (for Numbers of Snaking)
Interaction of Inner and Outer Modulus with Axial load are significant.
Interactions are similar in Length and Number of Snaking.
Interactions in case of amplitude, are not significant at all.
Interactions of Inner and outer modulus are not significant for NUM and AMP but it is significant for LEN.

## Slide 12: STAGE – II Machine Learning Prediction Models

## Slide 13: Procedure Employed to select Machine Learning Model -
Design the model and train it.
Optimize hyper-parameters to get the best cross-validation accuracy based on r2_score (Coefficient of Determination) and MSE (Mean Squared Error).
Consider the Importance of Accuracy, Speed, Interpretability and choose a Machine Learning model for each of the different output.

## Slide 14: Learning Curve for XGBoost Predictor for Number of Snaking (12 such graphs are there for various models and Output variables)

## Slide 15: SELECTION OF BEST MODELS
We have considered four factors that might help us to choose our model.
  Interpretability
  Training Speed
  Accuracy (Both of them)
Since dataset is small, training speed is not an issue for us.
Next slide will go through results of selection of best models.

## Slide 16: SELECTION OF MODELS -
Model | Interpret-ability |  | R2 Coefficient of Determination (Highest) | MSE |  | Training Speed
Number of Snaking |  |  |  |  |  | 
Linear Regression | High | 0.321 |  |  | 4.268 | High
SVR | Low | 0.545 |  |  | 2.856 | Low
Decision Tree(*) | High | 0.600 |  |  | 2.508 | High
XGBoost(**) | Low | 0.602 |  |  | 2.500 | Low
Global Length of Snaking |  |  |  |  |  | 
Linear Regression | High |  | 0.764 |  | 41.78 | High
SVR | Low |  | 0.873 |  | 23.32 | Low
Decision Tree (*) | High |  | 0.880 |  | 21.24 | High
XGBoost (**) | Low |  | 0.881 |  | 21.22 | Low
Snaking Amplitude |  |  |  |  |  | 
Linear Regression(*) | High |  | 0.708 |  | 0.495 | High
SVR | Low |  | 0.712 |  | 0.483 | Low
Decision Tree | High |  | 0.711 |  | 0.490 | High
XGBoost(**) | Low |  | 0.723 |  | 0.460 | Low

## Slide 17: Learning Curve Comparison
Below are three figure showing the learning curves of various ML Models.
(Left to Right : For Number of Snaking predictor, Snaking Length, Snaking amplitude.)

## Slide 18: Pareto Charts for Best Models
Below are three figure showing the Pareto charts of best Predictors (Left to Right : For Number of Snaking predictor, Snaking Length, Snaking amplitude.)
Used to measure visually see how well a model is performing by plotting the predicted values against true values.

## Slide 19: Stage – III Explainable AI

## Slide 20: Interpretability - LIME v/s SHAP
Better Interpretability Leads to Better Adoption
Initially, SHAP and LIME explainable AI methods. SHAP was considered more appropriate – Data Size.
LIME performs a Linear Regression in vicinity of the input data sample. - Contributions
SHAP computes the contribution of each feature to the final output of any sample
Important: Only gives info about Model structure.

## Slide 21: SHAP (SHapley Additive exPlanations)
The goal of SHAP is to explain the prediction of an instance x by computing the contribution of each feature to the prediction.
What is the Shapley Value?
  Contributions
Example
  Two people are to break stones. (A- 10, B-15 , together – 30 stones)
  But how much of these 30 stones were broken by A ? – (12.5 stones)
Order matters

## Slide 22: SHAP Results - Understanding
SHAP Summary Plot of Number of Snaking

## Slide 23: SHAP Summary Plot of Snaking length
SHAP Summary Plot of Snaking Amplitude

## Slide 24: Insights from SHAP -
The insights from SHAP mostly corroborates the pre-analysis but are easy to interpret.
Existence of threshold.
The impact is almost constant for all the other values of axial loads on number of snaking.
Friction factor behavior is as expected, extremely low contact for almost all the values.

## Slide 25
As shown in the dependence plot in figure, the impact of inner and outer modulus is significantly amplified for Axial Load = 6kN. Feature 0 is Inner Modulus in MPa, Feature 2 is Axial Load in kN.

## Slide 26: Other Activities -
Other models tested –
  Neural Network.
  Poisson Classification.
  Classification in case of number of snaking
    XGBoost and Decision tree.
  New data creation
    Randomized.

## Slide 27: NEXT STEPS
Optimization.
  We want to see the application of Bayesian Optimization in this setting.

## Slide 28: THE END.